## Slide 1: Business processes

## Slide 2
Break Down Maintenance
Corrective Maintenance
Preventive Maintenance
Refurbishment Maintenance
Calibration process

## Slide 3: Preventive Maintenance
To keep the downtimes and maintenance costs to a minimum the technical systems in a company are inspected and maintained regularly.
Types o preventive Maintenance:
Time – based :
Preventive maintenance tasks are triggered after a specific period of time has elapsed.
Ex: for every six months

## Slide 4
Performance –based:
PM tasks are triggered after specific performance level has been reached.
Ex: for every 10,000ltrs
Condition –based:
PM tasks are due when a condition is outside of a specific value range.
Ex: pressure lower than 15 bar or temperature higher than 85c.

## Slide 5: Preventive maintenance steps:
Task list
Maintenance plan
Scheduling the plan
Creation of maintenance orders
Technical completion of orders

## Slide 6: Types o Maintenance plans
Single cycle plan:
You create single cycle plans when you have to perform the same maintenance activities in full at regular intervals (time –based or performance –based)
Strategy plan:
You create strategy cycle plans when you have to perform the maintenance activities that are due at different intervals.
Multiple counter plan:
it depends on several influencing factors.

## Slide 7
Time –based single cycle plan:IP41
Scheduling parameters
Scheduling indicator
Scheduling period
Shift factors
Cycle modification factor
Call horizon

## Slide 8
Time –based strategy plan:IP42
You must include a task list specifically one that has strategy as the maintenance plan.
You define maintenance strategies using transaction ip11.
Strategy contains the chronology of packages
Packages define the frequency with which the operations has to be performed.

## Slide 9: Linear Asset Management
Linear assets are technical systems with a linear infrastructure whose properties and conditions can change from section to section.
ex:
Pipelines
Road networks
Rail networks
Power lines

## Slide 10
You can store the general linear data such as starting point , end point , length and unit of measurement.
You can assign linear data to functional location , equipment, notifications and orders.
In BNSF we have two types of Assets:
Linear assets: Assets which have different start and end points
Point assets : Assets which have same start and end points.

## Slide 11
You should have assigned suitable class and linear characteristics values for some particular mile post ranges .
LRP: Linear reference patterns are created to be able to assign a descriptive reference points to the real technical objects , thus you can send notifications such as “the damaged occurred 10km after some particular area.